NATIONAL OPEN UNIVERSITY OF NIGERIA

14/16 AHMADU BELLO WAY, VICTORIA ISLAND, LAGOS

SCHOOL OF SCIENCE AND TECHNOLOGY

JUNE/JULY EXAMINATION

COURSE CODE:  CIT852

COURSE TITLE:  Data Communication and Networks

TIME ALLOWED: 3 hrs

INSTRUCTION:   Attempt any Five (5) questions

  - Briefly explain the key features of the following:

    - Circuit-switched networks (2.5 marks)

    - Packaged-switched networks (2.5 marks)

  - State 3 advantages and 2 disadvantages of each of the following network topologies:

    - Bus (2.5 marks)

    - Star (2.5 marks)

    - Ring (2.5 marks)

  - List 3 types of broadcast networks (1.5 marks)

  - Complete the following table(3.5 marks):

| Layer | Data Package Name |
| --- | --- |
| Application |  |
| Presentation |  |
| Session |  |
| Transport |  |
| Network |  |
| Data-link |  |
| Physical |  |

  - With the aid of a table ONLY, outline 5 differences between the OSI reference model and the TCP/IP model.  (5 marks)

  - Define the following terms:

    - Baud (1 mark)

    - Noise (1 mark)

    - Propagation delay (1 mark)

    - Attenuation (1 mark)

  - For a constant rate transmission, if it takes 100 seconds to complete 1 transmission cycle, what is the frequency of the transmission?

  - State 3 drawbacks each of the TCP/IP reference model and the OSI reference model. (6 marks)

  - State 2 approaches to broadcast infrared networking.(2 marks)

  - State 3 characteristics of a connection-oriented service (3 marks)

  - List and explain very briefly 3 strategies to manage congestion in a network (3 marks)

  - State the 3 steps required for connection establishment in connection oriented services (3 marks).

  - Briefly explain the following concepts:

    - Flooding (3.5 marks)

    - Link state routing (4.5 marks)

  - State 3 reasons for congestion on a network (3 marks)

  - List the steps of the Djikstra routing algorithm (5 marks)

  - Using a table only, highlight 2 differences between congestion control and flow control. (4 marks)

  - For each class of IP address, specify the following with the aid of a table containing the following columns:	(5 marks)

    - IP address class

    - Higher order bit

    - Format

  - List the 4 types of routers identified by OSPF and state the function of each router (4 marks).

  - When an application invokes TCP, state and explain briefly what services it receives from TCP (6 marks).

  - State 3 important features of UDP (3 marks)

  - State 2 applications that use UDP exclusively (1 mark).

  - Explain the following terms:

    - Hierarchical address (1 mark)

    - Flat address (1 mark)

    - Static Address assignment (1.5 marks)

    - Dynamic address assignment (1.5 marks)

    - Adaptive routing (1.5 marks)

    - Non-adaptive routing (1.5 marks)

  - When routers receive packets faster than they can forward them, state the 2 possibilities that could occur in the case of congestion. (2 marks)

  - State 4 features of a token bucket traffic shaper. (4 marks)